## Slide 1: Department of Electrical & Electronics Engineering FUEL CELL BASED ULTRA-VOLTAGE GAIN BOOST CONVERTER FOR ELECTRIC VEHICLE APPLICATIONS
Presented by,
G Vinay Kumar (20P65A0222)
B Jhansi (19P61A0218)
B Vinay Kumar (19P61A0217)
B Sandeep (20P65A0205)
Under the guidance of,
Dr. B. Nagi Reddy M.Tech, PhD, MISRD
Associate Professor

## Slide 2: Contents
Abstract
Circuit Diagram
Operation
Designed Equations
Simulink diagram
Results
Observation from results
Conclusions
Applications
Future scope
References

## Slide 3: Abstract
A Fuel cell based Ultra-voltage Gain boost Converter is proposed for Electric vehicle Applications.
The main principle of this converter is to operate in a continuous conduction mode under steady-state analysis.
This converter includes two diodes, three inductors, two capacitors and three switches.
Project findings: It is able to achieve a higher voltage gain without having extreme duty cycle. Voltage boosting is much higher than a basic converter. Voltage and current stresses on the switches can be minimized and it enables us to select the devices with low rating, thus improving the overall efficiency of the system.

## Slide 4
Circuit Diagram
Fig.1 Fuel cell based ultra-voltage gain boost converter

## Slide 5
Mode 1:
This mode is activated once the switches are turned on, the three switches are turned on simultaneously.
In this mode, inductor LX is energized from the input dc-source, while inductors LY and LZ are energized from capacitor CX.
Diodes DX and DY are reversely biased.
Output capacitor CY releases its energy to the load side.
The characteristic equations that describe this mode of operation are as follows:
Operation

## Slide 6
Dept. of Electrical and Electronics Engineering
Fig.2 Mode-1 configuration of proposed converter

## Slide 7: Mode 2:
Dept. of Electrical and Electronics Engineering
This mode is activated once the switches are turned off, the three switches are turned off at the same time.
In this mode, inductor LX is discharging its energy into capacitor CX, while inductors LY and LZ are discharging their energy into output load and output capacitor CY.
In order to maintain a continuous path for the inductor currents, diodes DX and DY work as freewheeling diodes when they are turned on.
The characteristic equations that describe this mode of operation are as follows:

## Slide 8
Dept. of Electrical and Electronics Engineering
Fig.3 Mode-2 configuration of proposed converter

## Slide 9
Dept. of Electrical and Electronics Engineering
Designed Equations
Inductor Equations:
Inductor Lx Design:
LX
Inductor Ly and Lz Design:
LY
Voltage Gain M(D) = (1)

## Slide 10
Capacitor Equations:
Capacitor CX design:
Dept. of Electrical and Electronics Engineering
DTs …(5)
Capacitor CY Design:

## Slide 11: Components
Component | Description | Specification
Vin | Input Voltage | 20V
V0 | Output Voltage | 60V
LX | Inductor | 11.33µH
LY ,LZ | Inductors | 17.17µH
CX | Input Capacitor | 20.83µF
CY | Output Capacitor | 34 µF
R0 | Resistor | 1.44Ω
M(D) = V0/Vin | Gain | 3
D | Duty Ratio | 0.34
FS | Switching Frequency | 60000Hz
P0 | Rated Output Power | 2500W
Dept. of Electrical and Electronics Engineering
Table 1: Components of proposed converter

## Slide 12: Simulink diagram
Fig.4 MATLAB simulation of proposed converter

## Slide 13: Results
Simulated Waveform of Output voltage (V0):
Fig.5 Simulated waveform of V0 when D=0.34 & Vdc=20V

## Slide 14: Simulated Waveform of Output current (I0):
Dept. of Electrical and Electronics Engineering
Fig.6 Simulated waveform of I0 when D=0.34 & Vdc=20V

## Slide 15: Simulated waveforms of Switch voltages (VCHx , VCHy , VCHz ):
Dept. of Electrical and Electronics Engineering
Fig.8
Fig.7

## Slide 16
Dept. of Electrical and Electronics Engineering
Simulated waveforms of Diode Voltages(VDX , VDY):
Fig.10
Fig.9

## Slide 17: Simulated waveforms of Diode Currents (IDX , IDY):
Dept. of Electrical and Electronics Engineering
Fig.12
Fig.11

## Slide 18: Simulated waveforms of Inductor currents (ILX,ILY=ILZ):
Dept. of Electrical and Electronics Engineering
Fig.13
Fig.14

## Slide 19: Simulated waveforms of capacitor voltage(VCX ):
Dept. of Electrical and Electronics Engineering
Fig.15

## Slide 20: Performance of Proposed converter:
Dept. of Electrical and Electronics Engineering
D | VO | Io | Po | Pin | %η
10 | 25.9 | 18.03 | 468.23 | 489.6 | 95.6
15 | 30.38 | 21.09 | 640.71 | 671 | 95.4
20 | 35.66 | 24.77 | 883.29 | 928.4 | 95.1
25 | 42.11 | 29.25 | 1231.71 | 1301.4 | 94.6
30 | 49.97 | 34.7 | 1733.9 | 1847.6 | 93.8
34 | 57.56 | 39.97 | 2300.67 | 2476 | 92.91
35 | 59.67 | 41.44 | 2472.7 | 2668 | 92.6
40 | 71.59 | 49.72 | 3559.4 | 3912 | 90.9
45 | 82.26 | 57.12 | 4698.6 | 5276 | 89.05
50 | 89.24 | 61.98 | 5531 | 6340 | 87.7
55 | 97.34 | 67.6 | 6580.1 | 7752 | 84.8
60 | 106.9 | 74.2 | 7931.9 | 9692 | 81.8
Table 2: Performance of proposed converter

## Slide 21
Simulated Input power, Output power, power losses curve and Efficiency Curve:
Fig.16
Fig.17

## Slide 22: Switch Voltage Stresses of Proposed converter:
Dept. of Electrical and Electronics Engineering
D | VCHx(Th) | VCHx(si) | VCHy(Th) | VCHy(sim) | VCHz(Th) | VCHz(sim)
10 | 22.22222 | 22.28 | 24.69136 | 24.18 | 24.69136 | 24.18
15 | 23.52941 | 23.69 | 27.68166 | 26.82 | 27.68166 | 26.82
20 | 25 | 24.9 | 31.25 | 30.38 | 31.25 | 30.38
25 | 26.66667 | 26.6 | 35.55556 | 34.8 | 35.55556 | 34.8
30 | 28.57143 | 27.2 | 40.81633 | 39.8 | 40.81633 | 39.8
34 | 30.30303 | 30.35 | 45.91368 | 44.1 | 45.91368 | 44.1
35 | 30.76923 | 32.8 | 47.33728 | 45.4 | 47.33728 | 45.4
40 | 33.33333 | 35.5 | 55.55556 | 53.7 | 55.55556 | 53.7
45 | 36.36364 | 40.4 | 66.1157 | 60.7 | 66.1157 | 60.7
50 | 40 | 41.12 | 80 | 67.42 | 80 | 67.42
55 | 44.44444 | 46 | 98.76543 | 70.76 | 98.76543 | 70.76
60 | 50 | 54.4 | 125 | 77.2 | 125 | 77.2
Table 3: Comparison of theoretical and simulation values of Switch Voltage Stresses

## Slide 23
Dept. of Electrical and Electronics Engineering
Simulated Switch voltages vs Duty Ratio curve:
Fig.18

## Slide 24
Dept. of Electrical and Electronics Engineering
Inductor Currents vs Duty Ratio curves:
D | ILX | ILY | ILZ
10 | 24.48 | 20.11 | 20.11
15 | 33.55 | 24.83 | 24.83
20 | 46.42 | 31.25 | 31.25
25 | 67.46 | 39.88 | 39.88
30 | 95.48 | 50.75 | 50.75
34 | 127.3 | 62.4 | 62.4
35 | 137 | 65.9 | 65.9
40 | 200.1 | 86.4 | 86.4
45 | 269.3 | 109.35 | 109.35
50 | 322.8 | 131 | 131
55 | 394.1 | 157 | 157
60 | 491 | 194.1 | 194.1
Table 4: Inductor Currents
Fig.19

## Slide 25: Comparison with the existing converter topologies:
S.No | Converter | Number of inductors | Number of capacitors | Number of diodes | Number of power switches | Total number of components | Voltage gain
1 | Boost | 1 | 1 | 1 | 1 | 4 | 1/ (1 − D)
2 | SL Boost | 2 | 1 | 4 | 1 | 8 | (1+D)/ (1 − D)
3 | SC Boost | 1 | 3 | 1 | 1 | 6 | 1/ (1 − D)
4 | Non-isolated bidirectional DC-DC converter | 2 | 3 | 0 | 4 | 9 | 1/(1-D)^2
5 | A New High-Gain DC-DC Converter [24] | 2 | 2 | 2 | 2 | 8 | (1+D- 𝐷^2 )/(1 − 𝐷)^2
6 | An interleaved boost DC-DC converter [25] | 2 | 3 | 4 | 2 | 11 | 2/ (1 − D)
7 | Non-isolated high step-up DC–DC converters | 2 | 5 | 4 | 1 | 12 | (2+D)/ (1 − D)
8 | Single Switch High Step-Up DC–DC Converter [26] | 2 | 3 | 1 | 4 | 10 | (3+D)/2 (1 − D)
9 | Ultra voltage gain boost converter | 3 | 2 | 2 | 3 | 10 | (1+D)/(1 − 𝐷)^2
Table 5: Comparison with existing converter topologies

## Slide 26
D | Boost | SL Boost | SC Boost | Dual- Switch High- Boost DC– DC Converter | Non-isolated Bidirectional DC- DC converter [23] | A New High- Gain DC- DC Converter [24] | An Interleaved boost DC- DC converter [25] | Single Switch High Step- Up DC– DC Converter [26] | Ultra voltage gain boost converter
10 | 22.22 | 24.44 | 22.22 | 70 | 24.69 | 26.91 | 46.66 | 34.44 | 27.16
15 | 23.52 | 27.05 | 23.52 | 77.14 | 27.68 | 31.21 | 50.58 | 37.05 | 31.83
20 | 25 | 30 | 25 | 86.66 | 31.25 | 36.25 | 55 | 40 | 37.5
25 | 26.66 | 33.33 | 26.66 | 100 | 35.55 | 42.22 | 60 | 43.33 | 44.44
30 | 28.5 | 37.1 | 28.5 | 120 | 40.81 | 49.38 | 65.71 | 47.14 | 53.06
34 | 30.3 | 40.6 | 30.3 | 145 | 45.91 | 56.21 | 70.9 | 50.6 | 61.52
35 | 30.7 | 41.5 | 30.7 | 153.33 | 47.33 | 58.1 | 72.3 | 51.53 | 63.9
40 | 33.33 | 46.6 | 33.3 | 220 | 55.55 | 68.88 | 80 | 56.66 | 77.77
45 | 36.3 | 52.7 | 36.3 | 420 | 66.11 | 82.47 | 89.09 | 62.72 | 95.86
50 | 40 | 60 | 40 | In | 80 | 100 | 100 | 70 | 120
55 | 44.4 | 68.8 | 44.4 | -380 | 98.76 | 123.2 | 113.33 | 78.88 | 153.08
60 | 50 | 80 | 50 | -180 | 125 | 155 | 130 | 90 | 200
Comparison of Voltage Gain values with existing Converter topologies:
Table 6: Comparison of Voltage Gain

## Slide 27: Comparison of Voltage Gain curves with existing converter topologies:
Fig.20

## Slide 28: Comparison of Output Voltage values with existing converter topologies:
D | Boost | SL Boost | SC Boost | Dual- Switch High- Boost DC– DC Converter | Non-isolated Bidirectional DC- DC converter [23] | A New High- Gain DC- DC Converter [24] | An Interleaved boost DC- DC converter [25] | Single Switch High Step- Up DC– DC Converter [26] | Ultra voltage gain boost converter
10 | 22.22 | 24.44 | 22.22 | 70 | 24.69 | 26.91 | 46.66 | 34.44 | 27.16
15 | 23.52 | 27.05 | 23.52 | 77.14 | 27.68 | 31.21 | 50.58 | 37.05 | 31.83
20 | 25 | 30 | 25 | 86.66 | 31.25 | 36.25 | 55 | 40 | 37.5
25 | 26.66 | 33.33 | 26.66 | 100 | 35.55 | 42.22 | 60 | 43.33 | 44.44
30 | 28.5 | 37.1 | 28.5 | 120 | 40.81 | 49.38 | 65.71 | 47.14 | 53.06
34 | 30.3 | 40.6 | 30.3 | 145 | 45.91 | 56.21 | 70.9 | 50.6 | 61.52
35 | 30.7 | 41.5 | 30.7 | 153.33 | 47.33 | 58.1 | 72.3 | 51.53 | 63.9
40 | 33.33 | 46.6 | 33.3 | 220 | 55.55 | 68.88 | 80 | 56.66 | 77.77
45 | 36.3 | 52.7 | 36.3 | 420 | 66.11 | 82.47 | 89.09 | 62.72 | 95.86
50 | 40 | 60 | 40 | In | 80 | 100 | 100 | 70 | 120
55 | 44.4 | 68.8 | 44.4 | -380 | 98.76 | 123.2 | 113.33 | 78.88 | 153.08
60 | 50 | 80 | 50 | -180 | 125 | 155 | 130 | 90 | 200
Table 7: Comparison of output voltages

## Slide 29: Comparison of Output Voltage curves with existing topologies:
Fig.21

## Slide 30: Observations from the Results
The performance of the proposed converter in continuous current mode for steady state condition is analyzed.
From the simulation results, it can be observed that the proposed boost converter produces high voltage gain even for small duty ratios also (see fig.19).
The voltage and the current stresses of the proposed converter are lower when compared with the existing topologies. Therefore, the efficiency of the proposed converter is high for various duty ratios (see in Table 2).
Higher voltages with low ripple value is obtained (see in Table 3).

## Slide 31: Conclusions
The purpose of this project was to develop a new dc/dc boost configuration with high voltage-gain capability for fuel cell converters.
The developed configuration consisted of three switches, two diodes, and three inductors.
A theoretical analysis of the converter demonstrated its high voltage-gain, low voltage and current stress on its devices, and high efficiency.
The simulation results obtained were consistent with the theoretical analysis of the converter.

## Slide 32: Applications

## Slide 33: Future scope
The proposed converter has the features like increasing step-up gain voltage, continuous input current, increasing efficiency and less number of components.
Hence perfectly suitable for fuel cell system, photovoltaic applications and Electric vehicle applications.

## Slide 34: References
[1] Zaid, M.; Lin, C.-H.; Khan, S.; Ahmad, J.; Tariq, M.; Mahmood, A.; Sarwar, A.; Alamri, B.; Alahmadi, A. “ Family of transformerless quadratic boost high gain dc-dc converters”.Energies 2021, 14, 4372. [CrossRef]
[2] Barbosa, E.A.O.; Carvalho, M.R.S.D.; Rodrigues Limongi, L.; Cavalcanti, M.C.; Barbosa, E.J.; Azevedo, G.M.D.S. “High-gain high-efficiency dc–dc converter with single-core parallel operation switched inductors and rectifier voltage multiplier cell”. Energies 2021, 14, 4634. [CrossRef]
[3] Pereira, A.V.C.; Cavalcanti, M.C.; Azevedo, G.M.; Bradaschia, F.; Neto, R.C.; Carvalho, M.R.S.D."A novel single-switch high step-up dc–dc converter with threewinding coupled inductor”. Energies 2021, 14, 6288. [CrossRef]
[4] Souza, L.C.; Morais, D.C.; Silva, L.D.S.D.C.E.; Seixas, F.J.M.D.; Arenas, L.D.O. “DC-DC 3SSC-a-based boost converter: Analysis, design, and experimental validation”. Energies 2021, 14, 6771. [CrossRef]
[5] Gholizadeh, H.; Gorji, S.A.; Afjei, E.; Sera, “D. Design and implementation of a new cuk-based step-up DC–DC converter”. Energies 2021, 14, 6975. [CrossRef]
[6] Chub, A.; Vinnikov, D.; Blaabjerg, F.; Peng, F.Z. “A review of galvanically isolated impedance-source DC-DC converters”. IEEE Trans. Power Electron. 2016, 31, 2808– 2828. [CrossRef]
[7] Abdel-Rahim, O.; Chub, A.; Blinov, A.; Vinnikov, D. “New high-gain noninverting buck-boost converter”. In Proceedings of the IECON 2021–47th Annual Conference of the IEEE Industrial Electronics Society, Toronto, ON, Canada, 13 October 2021; pp. 1–6.
[8]. Ojeda-Rodríguez, Á.; González-Vizuete, P.; Bernal-Méndez, J.; Martín-Prats, M.A. “A survey on bidirectional dc/dc power converter topologies for the future hybrid and all electric aircrafts”. Energies 2020, 13, 4883. [CrossRef]
[9] De Souza, A.F.; Tofoli, F.L.; Ribeiro, E.R. Switched capacitor dc-dc converters: A survey on the main topologies, design characteristics, and applications. Energies 2021, 14, 2231. [CrossRef]
[10]. Forouzesh, M.; Siwakoti, Y.P.; Gorji, S.A.; Blaabjerg, F.; Lehman, B. Step-up DC-DC converters: A comprehensive review of voltage-boosting techniques, topologies, and applications. IEEE Trans. Power Electron. 2017, 32, 9143–9178. [CrossRef] FUEL CELL BASED ULTRA-VOLTAGE GAIN BOOST CONVERTER FOR ELECTRIC VEHICLE APPLICATIONS VBIT-EEE Page 42
[11]. Andrade, A.M.S.S.; Martins, M.L.D.S. “Quadratic-boost with stacked zeta converter for high voltage gain applications”. IEEE J. Emerg. Sel. Top. Power Electron. 2017, 5, 1787–1796. [CrossRef]
[12]. Ai, J.; Lin, M. “Ultra large gain step-up coupled-inductor dc-dc converter with an asymmetric voltage multiplier network for a sustainable energy system”. IEEE Trans. Power Electron. 2017, 32, 6896–6903. [CrossRef]
[13] Zhang, Y.; Gao, Y.; Zhou, L.; Sumner, M. “A switched-capacitor bidirectional dcdc converter with wide voltage gain range for electric vehicles with hybrid energy sources”. IEEE Trans. Power Electron. 2018, 33, 9459–9469. [CrossRef]

## Slide 35
[14] Axelrod, B.; Berkovich, Y.; Ioinovici, A. Switched-capacitor/switched-inductor structures for getting transformerless hybrid DC–DC pwm converters. IEEE Trans. Circuits Syst. 2008, 55, 687–696. [CrossRef]
[15] Young, C.-M.; Chen, M.-H.; Chang, T.-A.; Ko, C.-C.; Jen, K.-K. Cascade Cockcroft–Walton Voltage Multiplier Applied to Transformerless High Step-Up DC– DC Converter. IEEE Trans. Ind. Electron. 2013, 60, 523–537. [CrossRef]
[16] Andrade, A.M.S.S.; Hey, H.L.; Schuch, L.; da Silva Martins, M.L. Comparative Evaluation of Single Switch High-Voltage Step-Up Topologies Based on Boost and Zeta PWM Cells. IEEE Trans. Ind. Electron. 2018, 65, 2322–2334. [CrossRef]
[17] De Paula, W.J.; Júnior, D.D.O.; Pereira, D.D.; Tofoli, F.L. “Survey on non-isolated high-voltage step-up dc–dc topologies based on the boost converter”. IET Power Electron. 2015, 8, 2044–2057
[18] Waradzyn, Z.; Stala, R.; Mondzik, A.; Penczek, A.; Skala, A.; Pirog, S. “Efficiency Analysis of MOSFET-Based Air-Choke Resonant DC–DC Step-Up SwitchedCapacitor Voltage Multipliers”. IEEE Trans. Ind. Electron. 2017, 64, 8728–8738. [CrossRef]
[19] Cervera, A.; Evzelman, M.; Peretz, M.M.; Ben-Yaakov, S. “A high-efficiency resonant switched capacitor converter with continuous conversion ratio”. IEEE Trans. Power Electron. 2015, 30, 1373–1382. [CrossRef]
[20] Stala, R.; Waradzyn, Z.; Mondzik, A.; Penczek, A.; Skała, “A. DC–DC high stepup converter with low count of switches based on resonant switched-capacitor topology”. In Proceedings of the 2019 21st European Conference on Power Electronics and Applications (EPE’19 ECCE Europe), Genova, Italy, 2–5 September 2019; pp. P.1–P.10. FUEL CELL BASED ULTRA-VOLTAGE GAIN BOOST CONVERTER FOR ELECTRIC VEHICLE APPLICATIONS VBIT-EEE Page 43
[21] Shoyama, M.; Naka, T.; Ninomiya, T. “Resonant switched capacitor converter with high efficiency”. In Proceedings of the 2004 IEEE 35th Annual Power Electronics Specialists Conference 2004, Aachen, Germany, 20–25 June 2004; Volume 5, pp. 3780–3786. [CrossRef]
[22] Kesarwani, K.; Sangwan, R.; Stauth, J.T. “Resonant-switched capacitor converters for chip-scale power delivery: Design and implementation”. IEEE Trans. Power Electron. 2015, 30, 6966–6977. [CrossRef]
[23] Ardi, H.; Ajami, A.; Kardan, F.; Avilagh, S.N. “Analysis and implementation of a non-isolated bidirectional DC-DC converter with high voltage gain”. IEEE Trans. Ind. Electron. 2016, 63, 4878–4888.
[24] Ahmad, J.; Zaid, M.; Sarwar, A.; Lin, C.-H.; Asim, M.; Yadav, R.K.; Tariq, M.; Satpathi, K.; Alamri, B. “A New High-Gain DC-DC Converter with Continuous Input Current for DC Microgrid Applications”. Energies 2021, 14, 2629. [CrossRef]
[25] R. Gules, L. L. Pfitscher, and L. C. Franco, “An interleaved boost DC-DC converter with large conversion ratio,” in Proc. IEEE Int. Symp. Ind. Electron., 2003, pp. 411–416.
[26] Saravanan, S., & Babu, N. R. (2018). “Design and Development of Single Switch High Step-Up DC–DC Converter”. IEEE Journal of Emerging and Selected Topics in Power Electronics, 6(2), 855–863. doi:10.1109/jestpe.2017.2739819

## Slide 36: Queries

## Slide 37
THANK YOU